## Slide 1: Motor Circuit
Switch
Motor
Battery
Pack
Positive
Ground

## Slide 2: H-Bridge
GND
GND
Switch 2
Switch 4
Switch 1
Switch 3

## Slide 3: Pulse Width Modulation
Off
Slow
Medium
Fast
Fastest

## Slide 4: Motor Controller
Motor
Controller
Inputs
Outputs
High Power
Microcontroller
Motor 1
Motor 2
PWM
Low Power
PWM Signals
1 milliamp
High
Power
100 milliamps

## Slide 5: Microcontroller
Microcontroller
Digital Outputs
Program
Data
(RAM)
Inputs (sensors)
Digital
Analog
Motor
Controller
LEDs
Display
Speaker

## Slide 6: Breadboard
Power Rail
Columns
(Bus Strips)
component slot (center trough)
Red for +5 V
Blue (Black) for GND
Iinternal row connectors
Red column for 3.3 V
numbered rows run across
(horizontal center connections)
side columns share ground
and power
(vertical edge connections)

## Slide 7: Raspberry Pi Pico
$4.00 at Microcenter in St. Louis Park
264K SRAM (100x Arduino Uno)
2MB flash memory
26 × multi-function digital input or output pins
3 12-bit analogue inputs
16 controllable PWM channels
2 SPI, 2 I2C, and 2 UART channels
Accurate clock and timer on-chip
8 Raspberry Pi Programmable I/O (PIO) state machines
Temperature sensor
Dual core ARM Cortex-M0+ RISC processors
8 × Programmable I/O (PIO) state machines
Micro USB Connector

## Slide 8: Raspberry Pi Pico W (wireless)
$6.00 at Microcenter in St. Louis Park
All the same features as the Pico plus:
2.4GHz 802.11n wireless LA
Bluetooth will eventually also be supported (libraries missing)
Micro USB Connector
Wireless Chip

## Slide 9: Ultrasonic “Ping” Distance Sensor
HC-SR04 is a low-cost ultrasonic distance sensor that you can find for about $3.00
Uses “echolocation” to measure the time that a sound pulse takes to bounce off an object

## Slide 10: Time-of-Flight Distance Sensor
The VL53L0X is a low-cost ($3.00) time-of-flight sensor sends out a light pulse and measures the time it takes to bounce back
The sensor uses a IIC interface to send distance data to the microcontroller
Light travels about 1 foot every nanosecond so the stopwatch in the sensor must be accurate to the 1/100th of a nanosecond!
Distance = C * Time
2
C = 186,000 miles per second
Sensor
Target
Emitter
Receiver
Stopwatch

## Slide 11: Light Sensor Circuit
ADC_VREF - 3.3 Volts
Photoresistor
10K Resistor
AGND
GP26

## Slide 12: MicroPython
Many robot teaching labs are moving away from C/Arduino to MicroPython
Python is the most popular language in schools and the preferred language for most robotics projects
MicroPython has thousands of drivers and sample code for many devices
https://www.coderdojotc.org/micropython/

## Slide 13
https://www.codesavvy.org/
Coding Clubs
Code Savvy Explorer Clubs (Coder Dojo Twin Cities and Rebecca Coder Dojo)